# Fort Kent Commercial Wind Energy

# Facility Ordinance

# Enacted:  March 22, 2010.

# Table of Contents

Fort Kent Commercial Wind Energy	1

Facility Ordinance	1

Enacted:  March 22, 2010.	1

Table of Contents	2

1.0       Title	3

2.0       Authority	3

3.0       Purpose	3

5.0       Applicability	5

6.0       Conflict and Severability	5

8.0       Administration	6

a.         Application Forms	6

b.         Applications Fees	7

c.         Supporting Documents	7

8.8       Expiration of Permits	10

9.0       Application Submission Requirements	11

9.1       General Submission Requirements	11

9.2       Additional Submission Requirement for Type 2 and 3 Commercial Wind Energy 	  Facilities.		13

10.0     Meteorological Towers (MET Towers)	13

11.2     Building Permit	14

11.4     Electrical Components and Interconnections	14

11.7     Structure Type	15

11.8     Erosion Control	15

12.0     Special Standards for Commercial Wind Energy Facilities	15

12.1     Sound Limits	15

12.2     Discontinued Use	16

12.3     Use of Public Roads	16

12.4     Warnings	17

12.5     Artificial Habitat	17

12.6     Shadow Flicker	17

12.7     Local Emergency Services	17

12.8     Liability Insurance	17

12.9     Design Safety Certification	17

12.10   Public Inquiries and Complaints	18

12.11   Decommissioning	18

APPENDIX A	19

APPENDIX B	20

Fines	20

APPENDIX C	21

# 1.0       Title

This Ordinance shall be known as the Fort Kent Commercial Wind Energy Facility Ordinance.

# 2.0       Authority

This Ordinance is adopted pursuant to the enabling provisions of Article VIII, Part 2, Section 1 of the Maine Constitution; the provisions of 30-A M.R.S.A..§3001 (Home Rule), and the provisions of the Planning and Land Use Regulation Act, 30-A M.R.S.A. § 4312 et. seq.

# 3.0       Purpose

The purpose of the Ordinance is to provide for the construction and operation of Commercial Wind Energy Facilities in the Town of Fort Kent, subject to reasonable conditions that will protect the public health, safety, and welfare.

4.0       Definitions

Applicant is the legal entity, including successors and assigns, that files an application under this Ordinance.

Approved Residential Subdivision means a residential subdivision for which all applicable land use permits have been issued, provided that the time for beginning construction under such permits has not expired.

Associated Facilities means elements of a Wind Energy Facility other than its generating facilities that are necessary to the proper operation and maintenance of the Wind Energy Facility, including but not limited to buildings, access roads, generator lead lines and substations.

Commercial Wind Energy Facility means a facility that uses one or more turbines to convert wind energy to electrical energy and has a maximum generating capacity in excess of 100kw.  A Commercial Wind Energy Facility includes Generating Facilities and Associated Facilities.

Commercial Wind Energy Facility Type 1 means a Commercial Wind Energy Facility having a maximum generating capacity in excess of 100 kw.

Commercial Wind Energy Facility Type 2 means a Commercial Wind Energy Facility having a maximum generating capacity in excess of 100 kw and requiring Maine Department of Environmental Protection Siting Certification for Small-Scale Wind Energy Developments pursuant to 35-A M.R.S.A. § 3456.

Commercial Wind Energy Facility Type 3 means a Commercial Wind Energy facility 	having a maximum generating capacity in excess of 100 kw and requiring a State of Maine 	Site Location of Development permit.

DEP Certification means a certification issued by the Department of Environmental 	Protection pursuant to 35-A M.R.S.A.. § 3456 for a Wind Energy Development.

Generating Facilities means Wind Turbines and electrical lines, not including Generator 	Lead Lines, that are immediately associated with the Wind Turbines.

Generator Lead Line means a “generator interconnection transmission facility” as defined by 	35-A.M.R.S. § 3132 (1-B).

Meteorological Tower (MET Tower) means a Tower used for the measurement and 	collection of wind data that supports various types of equipment, including but not limited to 	anemometers, data recorders, and solar power panels. MET Towers may also include wildlife 	related equipment such as ANABAT detectors, bird diverts and wildlife entanglement 	protectors.

Municipal Reviewing Authority means the Fort Kent Planning Board.

Nacelle means the frame and housing at the top of the Tower that encloses the gearbox and 	 generator.

Non-Participating Landowner means any landowner, other than a Participating Landowner 	whose land is located within the Town of Fort Kent.

Occupied Buildings means a residence, school, hospital, house of worship, public library or 	other building that is occupied or in use as a primary residence or is customarily frequented 	by the public at the time when the permit application is submitted.

Participating Landowner means one or more Persons that hold title in fee or a leasehold 	interest with sublease rights to property on which Generating Facilities or Associated 	Facilities are proposed to be located pursuant to an agreement with the Applicant or an entity 	that has entered into an appropriate agreement with the Applicant allowing the Applicant to 	demonstrate the requisite right, title and interest in such property.

Person means an individual, corporation, partnership, firm, organization or other legal entity.

Shadow Flicker means alternating changes in light intensity caused by the movement of 	Wind Turbine blades casting shadows on the ground or a stationary object.

Short Duration Repetitive Sounds means a sequence of repetitive sounds which occur more 	than once within an hour, each clearly discernible as an event and causing an increase in the 	sound level of at least 6 dBA on the fast meter response above the sound level observed 	immediately before and after the event, each typically less than ten seconds in duration, and 	which are inherent to the process or operation of the development and are foreseeable.

Substantial Start means that construction shall be considered to be substantially commenced 	when any work beyond excavation, including but not limited to, the pouring of a slab or 	footings, the installation of piles, the construction of columns, or placement of a Tower on a 	foundation has begun.

Tower means the free-standing structure on which a wind measuring or energy conversion 	system is mounted.

Turbine Height means the distance measured from the surface of the Tower foundation to 	the highest point of any turbine rotor blade measured at the highest arc of the blade.

Wind Turbine means a system for the conversion of wind energy into electricity which is 	comprised of a Tower, generator, Nacelle, rotor and transformer.

# 5.0       Applicability

5.1       	This Ordinance applies to any Commercial Wind Energy Facility proposed for 			construction in the Town of Fort Kent after the effective date of this Ordinance. This 		Ordinance does not apply to Associated Facilities unless the Generating Facilities are 		located within the Town of Fort Kent, in which case this Ordinance applies to both 		the Generating Facilities and the Associated Facilities.

5.2      	 A Commercial Wind Energy Facility that is the subject of an application determined 		to be complete by the Fort Kent Planning Board prior to the effective date of this 			Ordinance shall not be required to meet the requirements of this Ordinance; provided 		that any physical modifications after the effective date of the Ordinance shall be 			subject to the permitting requirements of Section 8.2.

# 6.0       Conflict and Severability

6.1      	 If there is a conflict between provisions in this Ordinance, the more stringent shall 		apply. If there is a conflict between a provision in this Ordinance and that of another 		Town of Fort Kent ordinance, the provision of this Ordinance shall apply.

6.2       	The invalidity of any part of this Ordinance shall not invalidate any other part of this 		ordinance.

7.0       Effective Date

This Ordinance becomes effective on March 23, 2010.

# 8.0       Administration

8.1       Review and Approval Authority

1.         The Code Enforcement Officer is authorized to review all applications for 			Commercial Wind Energy Facilities for completeness prior to submission to 			the Fort Kent Planning Board.

2.         The Fort Kent Planning Board is authorized to review all applications for 				Commercial Wind Energy Facilities and may approve, deny or approve such 			applications with conditions in accordance with this Ordinance.

8.2       Permit Required

1.         No Commercial Wind Energy Facility shall be constructed or located within 			the Town of Fort Kent without a permit issued in accordance with this 				Ordinance.

2.         Any physical modifications to an existing Commercial Wind Energy Facility 			that materially alters the location or increases the area of development on the 			site or that increases the Turbine Height or the level of sound emissions of any 			Wind Turbine shall require a permit modification under this Ordinance. Like-			kind replacements and routine maintenance and repairs shall not require a 				permit modification.

8.3       Permit Applications

1.         Application Components

A Commercial Wind Energy Facility permit application shall consist of the 			application form, application fee, and supporting documents as described 				below:

# a.         Application Forms

The municipality shall provide the application form which shall be 				signed by:

1) a Person with right, title, and interest in the subject property 					or;

2) a Person having written authorization from a Person with 		right, title and interest in the subject property. The signature 		shall be dated and the signatory shall certify 	that the 			information in the application is complete and correct, and that 		the proposed facility will be constructed and operated in 			accordance with the standards of this ordinance and all 			approval and permit conditions, if any.

# b.         Applications Fees

Application fees shall be assessed and paid upon submission of the 				application in accordance with Appendix A of this Ordinance, which 				shall be revised by the Fort Kent Town Council as necessary.

# c.         Supporting Documents

The applications shall include all additional documents necessary to 				satisfy the applicable submission requirements under Section 9 of this 				Ordinance.

2.         Application Submission. The Applicant shall submit its application for a 				Commercial Wind Energy Facility permit to the Code Enforcement Officer 			who shall note on the application the date on which it was received.

3.         Changes to a Pending Application

a.         The Applicant shall promptly notify the Fort Kent Planning Board of 				any changes the Applicant proposes to make to information contained 				in the application.

b.         If changes are proposed to a pending application after a public hearing 				 has been held, the Fort Kent Planning Board may consider those  					changes and continue with the review and approval process without a 				renewed public hearing if it determines that the changes do not 					materially alter the application. If the Fort Kent Planning Board 					determines that the proposed changes do materially alter the 					application it shall schedule and conduct another public hearing within 				30 days of that determination. In making its determination, 	the Fort 				Kent Planning Board shall consider whether the proposed changes 					involve potential adverse effects different than or in addition to those 				addressed in the initial application.

8.4       Permit Application Procedures

1.         Commercial Wind Energy Facility Applications

a.         The Applicant is strongly encouraged to meet with the Code 					Enforcement Officer before submitting an application. At this pre-					application meeting, the Code Enforcement Officer will explain the 				Ordinance’s provisions, application forms, and submission 						requirements. The Applicant should provide photos of the proposed 				site and written descriptions of the proposed facility and the proposed 				site, including its location and lot area.

b.        Within 30 days after receipt of the application by the Code 						Enforcement Officer, the Fort Kent Planning Board shall notify the 				Applicant in writing either that the application is complete or, if the 				application is incomplete, the specific additional material needed to 				complete the application. The Fort Kent Planning Board may waive 				any submission requirement if it issues a written finding that, due to 				special circumstances of the application, adherence to that requirement 				is not necessary to determine compliance with the standards of this 				Ordinance.

c.         The Fort Kent Planning Board shall hold a public hearing for a 					Commercial Wind Energy Facility application within 60 days after 				determining that the application is complete.

d.         Within 90 days after determining that an application for a Commercial 				Wind Energy Facility is complete, the Fort Kent Planning Board shall 				issue a written order:

1) denying approval of the proposed Commercial 							Wind Energy Facility,

2) granting approval of the proposed Commercial Wind Energy 					Facility or,

3) granting approval of the proposed 	Commercial Wing 						Energy Facility with conditions. In making its decision, the 						Fort Kent Planning Board shall make findings on whether the 					proposed Commercial Wind Energy Facility meets the 						applicable criteria described in sections 11 and 12.

e.          With the agreement of the applicant, the Fort Kent Planning Board 				may extend the procedural time frames of this section.

8.5       Notice of Meetings

Fourteen days prior to any meeting at which an application for a Commercial Wind 		Energy Facility is to be considered, the Fort Kent Planning Board shall send notice by 		first class mail, to the applicant and all owners of property abutting the property on 		which the Commercial Wind Energy Facility is proposed to be located. The notice 		shall state the date, time and place of the meeting and the proposed location of the 		Commercial Wind Energy Facility.

8.6       Public Hearings

The Fort Kent Planning Board shall have notice of the date, time, and place of any 		public hearing and the proposed location of the proposed Commercial Wind Energy 		Facility:

a.         Published at least once in a newspaper having general circulation within the 			municipality. The date of the first publication shall be at least 14 days before 			the hearing.

b.         Mailed by first class mail to the applicant and to owners of property abutting 			the property on which the Commercial Wind Energy Facility is proposed to be 			located, at least 14 days before the public hearing. The Fort Kent Planning 			Board shall maintain a list of property owners to whom notice is mailed in the 			application file. Failure of any of these property owners to receive a notice 			shall not invalidate the public hearing, nor shall it require the Fort Kent 				Planning Board to schedule another hearing.

8.7       Professional Services

Applicants shall pay all costs associated with the review and processing of the 			application, and shall submit a fee with the application in an amount as set by the Fort 		Kent Town Council. In addition to such application fees as set by the Councilors, the 		Town of Fort Kent shall require the applicant to pay extra fees incurred to cover the 		Town’s costs of reviewing and processing the application. This shall include, but is 		not limited to, the Town’s ordering additional scientific studies, and the Town 			engaging the services of one or more professional engineers and others 				including, but not limited to an attorney or consultant with required professional 			expertise to independently review on the behalf of the Town the technical information 		provided in the application and to assist the Town in processing the application. The 		applicant, upon request, shall promptly submit such extra fee(s). Following action on 		the application, any unused amount of the extra fee(s) shall be returned to the 			applicant with a summary of the costs incurred.

# 8.8       Expiration of Permits

Permits shall expire:

1) two years after the date of approval unless a substantial start on construction has 		occurred and;

2) three years after the date of approval unless construction of the Commercial Wind 		Energy Facility has been completed.  If a permit for a Commercial Wind Energy 			Facility expires, the applicant shall implement pertinent provisions of the approved 		decommissioning plan. Upon the applicant’s written request, the Fort Kent Planning 		Board may extend either or both expiration time limits by one year.

8.9       Access

The Code Enforcement Officer shall have access to the site at all times to review the 		progress of the work and shall have the authority to review all records and documents 		directly related to the design, construction and operation of the facility

8.10     Enforcement

1.  It shall be unlawful for any Person, to violate or fail to comply with or take any 		action that is contrary to the terms of the Ordinance, or to violate or fail to comply 		with any permit issued under the Ordinance, or to cause another to violate or fail to 		comply or take any action which is contrary to the terms of the Ordinance or any 			permit under the Ordinance.

2.  If the Code Enforcement Officer or other Person charged with enforcement of 			municipal laws determines that a violation of the Ordinance or the permit has 			occurred, the Code Enforcement Officer shall provide written notice to any Person 		alleged to be in violation of this Ordinance or permit. If the alleged violation does not 		]pose an immediate threat to public health or safety, the Town of Fort Kent and the 		alleged violator shall engage in good faith negotiations to resolve the alleged 			violation. Such negotiations shall be conducted within thirty (30) days of the notice of 		violation and, with consent of the alleged violator may be extended.

3.  If after thirty (30) days from the date of notice of violation or further period as 		agreed to by the alleged violator the Code Enforcement Officer determines, in the 			officer’s reasonable discretion, that the parties have not resolved the alleged violation, 		the Code Enforcement Officer may institute a stop work order proceedings or any 			other remedy at law to ensure compliance with the Ordinance or permit, or assess any 		applicable fines as established by the Fort Kent Town Council as set forth in 			Appendix B of this Ordinance, which shall be revised by the Fort Kent Town Council 		as necessary.

8.11     Appeals

Any Person aggrieved by a decision of the Code Enforcement Officer or Fort Kent 		Planning Board under this Ordinance may appeal the decision to the Fort Kent 			Zoning Board of Appeals, as provided by Section 12 of the Town of Fort Kent 			Zoning Ordinance.

# 9.0       Application Submission Requirements

# 9.1       General Submission Requirements

1.      A completed application form including:

a.  The Applicant and Participating Landowner(s)’ names(s) and contact 				information.

b.  The address, tax map number, zone and owner(s) of the proposed facility 			site and any contiguous parcels owned by Participating Landowners.

c.  The tax map number, zone, current use, owner(s) and addresses of 				owner(s) of parcels that abut the proposed facility site or abut parcels of 				Participating Landowners that are contiguous with the proposed facility site.

d.  An affirmation, signed and dated by the Applicant, that the information 			provided in the application is correct and that the proposed Commercial Wind 			Energy Facility, if approved and built, shall be constructed and operated in 			accordance with the standards of this ordinance and all conditions of approval, 			if any.

2.         Receipt showing payment of application fee in accordance with Appendix A.

3.         A copy of a deed, easement, purchase option or other comparable 					documentation demonstrating that the Applicant has right, title or interest in 			the subject property.

4.         Location map showing the boundaries of the proposed facility site and of all 			contiguous property under total or partial control of the Participating Owner 			or Applicant or Participating Landowner(s).

5.         Description of the proposed Commercial Wind Energy Facility that includes 			the number and aggregate generating capacity of all Wind Turbines, the 				Turbine Height and manufacturer’s specifications for each Wind Turbine 				(including but not limited to the make, model, maximum generating capacity, 			and sound emission level and types of over speed controls) and a description 			of Associated Facilities.

6.         Site plan showing the proposed location of each Wind Turbine and 				Associated Facilities and any of the following features located within 500 feet 			of any Wind Turbine:  parcel 	boundaries, required setbacks, topographic 				contour lines (maximum 20-foot interval), roads, driveways, rights-of-way, 			overhead utility lines, buildings (identified by use), land cover, wetlands, 				streams, water bodies and areas proposed to be re-graded or cleared of 				vegetation.

7.         Written evidence that the Environmental Coordinator of the Maine 					Department of Inland Fisheries and Wildlife (MDIFW) and that the Maine 			Natural Areas Program (MNAP) have both been notified of the pending 				application and the location and Turbine Height of all proposed Wind 				Turbines.

8.         Description of emergency and normal shutdown procedures.

9.         Written evidence that the provider of electrical service to the property has 			been notified of the intent to connect an electric generator to the electricity 			grid, if such connection is proposed.

10.       Photographs of existing conditions at the site.

11.       Applications shall also include the Wind Turbine manufacturer’s noise 				emission specifications.

12.       Applications shall also include Structural drawings of the Tower foundation 			and anchoring system prepared by the Wind Turbine or Tower manufacturer 			or in accordance with the manufacturer’s specifications, or stamped by a 				licensed structural engineer.

13.       Applications shall also include, if applicable and issued at the time of 				application, certification from the Department of Environmental Protection 			pursuant to Title 35-A M.R.S. section 3456 that the Wind Energy Facility:

a.         Will meet the requirements of the noise control rules adopted by the 				Board of Environmental Protection pursuant to Title 38 M.R.S.A. 					Chapter 3, subchapter 1, article 6;

b.         Will be designed and sited to avoid unreasonable adverse Shadow 					Flicker effects; and

c.         Will be constructed with setbacks adequate to protect public safety.

If such certification has not been issued at the time of application, the 				Applicant shall include written evidence that the certification has been 				requested.

# 9.2       Additional Submission Requirement for Type 2 and 3 Commercial Wind Energy 			Facilities.

1.         Certificates of design compliance obtained by the equipment manufacturers 			from Underwriters Laboratories or other similar certifying organizations.

2.         A Decommissioning plan in conformance with Appendix C.

3.         Written summary of operation and maintenance procedures for the Wind 				Energy Facility and a maintenance plan for access roads, erosion and 				sedimentation controls and storm water management facilities.

4.         Standard boundary survey of the subject property stamped by a Maine-				licensed surveyor. The Fort Kent Planning Board may waive this requirement 			if it determines that the Applicant has provided information sufficient to 				identify property boundaries to the extent necessary.

5.         Storm water management plan stamped by a Maine-licensed professional 				engineer.

6.         Sound level analysis, prepared by a qualified engineer that addresses the 				standards of section 12.1.

7.         Shadow Flicker analysis based on modeling software approved by the 				Department of Environmental Protection.

8.         Foundation and anchoring system drawings that are stamped by a Maine-				licensed professional engineer.

9.         Other relevant studies, reports, certifications and approvals as may be 				reasonably requested by the Fort Kent Planning Board to ensure compliance 			with this Ordinance.

# 10.0     Meteorological Towers (MET Towers)

Applications for Meteorological (MET) Towers shall be reviewed and permits issued by the 	Fort Kent Planning Board. Within 30 days following removal of a MET Tower, the 	Applicant shall restore the site to its original condition to the extent practicable. The 		provisions of this section do not apply to permanent MET Towers included as Associated 	Facilities in approved Wind Energy 	Facilities applications.

11.0     General Standards

11.1     Safety Setbacks/Maximum Height

Wind Turbine Towers shall be set back from property boundaries, public and private 		rights-of-way and overhead utility lines that are not part of the proposed generating 		facility; a horizontal distance equivalent to 150% of the Turbine Height. Wind 			Turbine Towers shall be set back from occupied buildings on non-participating 			landowner property a horizontal distance equivalent to 250% of the turbine height.

The maximum turbine height (see Definitions) for any project constructed in the 			Town of Fort Kent shall be 450 feet. The total or maximum height will take into 			account the tower, generator, 	nacelle, rotor, and transformer.

# 11.2     Building Permit

All components of the Commercial Wind Energy Facility shall conform to relevant 		and applicable local and state building codes.

11.3     Overspeed Controls and Brakes

Each Wind Turbine shall be equipped with an overspeed control system that: 1) 			includes both an aerodynamic control such as stall regulation, variable blade pitch, or 		other similar system, and a mechanical brake that operates in fail safe mode; or 2) has 		been designed by the manufacturer or a licensed civil engineer and found by the 			municipal entity responsible for review and approval of the application under 8.1, 			based on its review of a written description of the design and function of the system, 		to meet the needs of public safety.

# 11.4     Electrical Components and Interconnections

All electrical components of the Commercial Wind Energy Facility shall conform to 		relevant and applicable local, state, and national codes.

11.5     Access

All ground-mounted electrical and control equipment and all access doors to a Wind 		Turbine shall be labeled and secured to prevent unauthorized access. A Wind Tower 		shall not be climbable up to a minimum fifteen (15) feet above ground surface.

11.6     Signal Interference

The Applicant shall make reasonable efforts to avoid and mitigate to the extent 			practicable any disruption or loss of radio, telephone, television, or similar signals 		caused by the Commercial Wind Energy Facility. A Commercial Wind Energy 			Facility shall not interfere with existing communication facilities for police and 			emergency services.

# 11.7     Structure Type

With the exception of Meteorological (MET) Towers, Towers shall be monopoles 		with no guy wires.

# 11.8     Erosion Control

Erosion of soil and sedimentation shall be minimized by employing “best 				management practices” in the “Maine Erosion Control Handbook for Construction: 		Best Management Practices”, March 2003, or its most current edition.

11.9     Visual Appearance

1.         A Wind Turbine shall be a non-obtrusive color such as white, off-white or 			gray, or as may otherwise be required by another governmental agency with 			jurisdiction over the Commercial Wind Energy Facility.

2.         A Wind Turbine shall not be lighted artificially, except to the extent 				consistent with Federal Aviation Administration recommendations or other 			applicable authority that regulates air safety or as is otherwise required by 				another governmental agency with jurisdiction over the Wind Energy Facility.

3.         A Wind Turbine shall not be used to support signs and shall not display 				advertising except for reasonable and incidental identification of the turbine 			manufacturer, facility owner and operator, and for warnings.

# 12.0     Special Standards for Commercial Wind Energy Facilities

# 12.1     Sound Limits

Sound levels of Commercial Wind Energy Facilities shall not exceed a maximum of 		45 dBA measured at non-participating landowners property lines and shall not exceed 		a maximum of 42 dBA measured at occupied buildings on non-participating 			landowners property. Sound emissions shall comply with all other requirements 			described in Chapter 375, Section 10 of the rules promulgated by the Board of 			Environmental Protection concerning the Site Location of Development Law if 			applicable to applicant’s project.

# 12.2     Discontinued Use

1.         A Commercial Wind Energy Facility that is not generating electricity for 				twelve (12) consecutive months shall be deemed a discontinued use and shall 			be removed from the property by the Applicant within 120 days of receipt of 			notice from the Code Enforcement Officer, unless the Applicant provides 				information that the Fort Kent Planning Board deems sufficient to 					demonstrate that the project has not been discontinued and should not be 				removed. If the Commercial Wind Energy Facility is not removed within this 			time period, the municipality may remove the turbine(s) at the Applicant’s 			expense. The Applicant shall pay all site reclamation costs deemed necessary 			and reasonable to return the site to its pre-construction condition, including 			the removal of roads and reestablishment of vegetation.

2.         If a surety has been given to the municipality for removal of the Commercial 	Wind Energy Facility, the Applicant may apply to the Fort Kent Planning 	Board for release of the surety when the Commercial Wind Energy Facility 	has been removed to the satisfaction of the Code Enforcement Officer.

# 12.3     Use of Public Roads

1.  The Applicant shall identify all state and local public roads to be used 		within the Town of Fort Kent to transport equipment and parts for 			construction, operation or maintenance of a Commercial Wind Energy 		Facility.

2.  The Town Road Commissioner or a qualified third-party engineer 			reasonably acceptable to both the Fort Kent Planning Board and the 		Applicant and paid for by the 	Applicant pursuant to Section 8.7 of the 		Ordinance, shall document road conditions prior to construction. The 		Town Road Commissioner or third-party engineer shall document road 		conditions again thirty (30) days after construction is complete or as 		weather permits.

3.   The Applicant shall demonstrate, to the satisfaction of the Fort Kent 		Planning Board that it has financial resources sufficient to comply with 		subsection 4, below, and the Fort Kent Planning Board may require the 		Applicant to post a bond or other security in order to ensure such 			compliance.

4.   Any road damage caused by the Applicant or its contractors shall be 		promptly repaired at the Applicant’s expense.

# 12.4     Warnings

A clearly visible warning sign concerning voltage must be placed at the base of all 		pad-mounted transformers and substations.

# 12.5     Artificial Habitat

To the extent practicable, the creation of artificial habitat for raptors or raptor prey 		shall be minimized. In making its determination under this subsection the Fort Kent 		Planning Board shall  consider comments and recommendations, if any provided by 		the Maine Department of Inland Fisheries and Wildlife.

# 12.6     Shadow Flicker

Commercial Wind Energy Facilities shall be sited and designed to avoid 				unreasonable adverse shadow flicker effect at any Occupied Building located on a 		Non-Participating Landowner’s property.

# 12.7     Local Emergency Services

1.  The Applicant shall provide a copy of the project summary and site plan to local 		emergency service providers.

2.  Upon request, the Applicant shall cooperate with emergency service providers to 		develop and coordinate implementation of an emergency response plan for a 			Commercial Wind Energy Facility.

3.  A Wind Turbine shall be equipped with an appropriate fire suppression system to 		address fires within the Nacelle portion of the turbine or shall otherwise address the 		issue of fire safety to the satisfaction of the Fort Kent Planning Board.

# 12.8     Liability Insurance

The Applicant or an Applicant’s designee acceptable to the Fort Kent Planning 			Board shall maintain a current general liability policy for the Commercial Wind 			Energy Facility that covers bodily injury and property damage with limits in an 			amount commensurate with the scope and scale of the Facility. The Applicant or its 		designee shall make certificates of insurance available to the Fort Kent Planning 			Board upon request.

# 12.9     Design Safety Certification

Each Wind Turbine shall conform to applicable industry standards including those of 		the American National Standards Institute (ANSI) and at least one of the following: 		Underwriters Laboratories, or other similar certifying organization.

# 12.10   Public Inquiries and Complaints

1.  The Applicant or its designee shall maintain a phone number and identify a 			responsible Person for the public to contact with inquires and complaints throughout 		the life of the Commercial Wind Energy Facility.

2.  The Applicant or its designee shall make reasonable efforts to respond to the 			public’s inquiries and complaints and shall provide written copies of all complaints 		and the company’s resolution upon request.

# 12.11   Decommissioning

The Applicant for a Type 3 Commercial Wind Energy Facility shall prepare and fund 		a decommissioning plan in conformance with Department of Environmental 			Protection’s submission requirements for a permit pursuant to the Site Location of 		Development Law, 38 M.R.S.A. Sections 481-490, as set forth in Appendix C.

# APPENDIX A

Application Fees

# APPENDIX B

# Fines

# APPENDIX C

Decommissioning Plan

Pursuant to section 12.11, the Applicant shall provide a plan for decommissioning a Commercial Wind Energy Facility. The decommissioning plan shall include, but shall not be limited to the following:

1.   A description of the trigger for implementing the decommissioning plan. There is a rebuttable presumption that decommissioning is required if no electricity is generated for a continuous period of twelve (12) months. The Applicant may rebut the presumption by providing evidence, such as a force majeure event that interrupts the generation of electricity, that although the project has not generated electricity for a continuous period of 12 months, the project has not been abandoned and should not be decommissioned.

2.  A description of the work required to physically remove all Wind Turbines, associated foundations to a depth of 24 inches, buildings, cabling, electrical components, and any other Associated Facilities to the extent they are not otherwise in or proposed to be placed into productive use. All earth disturbed during decommissioning must be graded and re-seeded, unless the landowner of the affected land request otherwise in writing.

[Note:  At the time of decommissioning, the Applicant may provide evidence of plans for 	continued beneficial use of any or all of the components of the Wind Energy Facility. Any 	changes to the 	approved decommissioning plan shall be subject to review and approval by 	the Code Enforcement Officer].

3. An estimate of the total cost of decommissioning of the equipment and itemization of the estimated major expenses, including the projected costs of measures taken to minimize or prevent adverse effects on the environment during implementation of the decommissioning plan. The itemization of major costs may include, but is not limited to, the cost of the following activities: turbine removal, turbine foundation removal and permanent stabilization, building removal and permanent stabilization, transmission corridor removal and permanent stabilization and road infrastructure removal and permanent stabilization.

4.  Demonstration in the form of a performance bond, surety bond, letter of credit, parental guarantee or other form of financial assurance as may be acceptable to the Fort Kent Planning Board that upon the end of the useful life of the Commercial Wind Energy Facility the Applicant will have the necessary financial assurance in place for 100% of the total cost of decommissioning. The Applicant may propose securing the necessary financial assurance in phases, as long as the total required financial assurance is in place a minimum of 5 years prior to the expected end of the useful life of the Commercial Wind Energy Facility.